## Purpose

To provide general information on and provide general guidelines to follow while training for and performing operations involving rescue from confined spaces.

## Scope

Covers all aspects of confined space rescue. A line officer has the authority to modify this SOG as the emergency or training situation dictates.

## Training

- The training schedule for qualification as a confined space rescuer is as follows:

  - Training may only start after the trainee has successfully completed firefighter 1.

  - Trainee must complete

    - a County, State or other recognized and accredited confined space awareness course

    - a County, State or other recognized and accredited confined space operations course

    - a CPR/AED course

    - a First Aid, First Responder, or EMT course

  - Once qualified, firefighters must

    - Attend a minimum of 1 in-house confined space rescue drill annually.

    - Possess a valid CPR/AED card

    - Posses a valid First Responder or EMT certification

## Dispatching

- Upon receiving an emergency call, requesting a confined space rescue, Somerset County Communications (SCC) shall follow Franklin Township Dispatch protocols and the SCC Mutual Aid guide.

## Responding

- Responding units should contact SCC

  - For updates on the nature of the call in order to gain as much information as possible prior to arrival

  - To request that a witness or competent person on scene meet the first arriving units upon their arrival

## Arrival on Scene

- If Incident Command (IC) has already been established, the officer of Rescue 56 should assume the role of Operations Section Chief.

- If IC has not been established, the officer of Rescue 56 should assume the role of IC until command can be transferred.  If the officer of Rescue 56 is acting as IC, the officer shall delegate the role of Operations Section Chief to the most experienced member on his/her crew.

## Size up

- The first arriving officer at the scene of a confined space incident shall initiate the process of filling in the confined space entry /rescue permit.

- As soon as possible the IC shall appoint an officer or firefighter as a scribe. The role of the scribe is to fill out the entry/rescue permit as conditions and information become available.

- A blank copy of the permit should also be given to the operations officer, EMS officer, safety officer and haz mat officer so they can use it as a guideline. They should relay pertinent information to IC so the scribe can record the information.

- No entry shall be made into the confined space until Phase 1, 2 and 3 of the permit has been reviewed and completed.

## Rescue Operations

- Follow the steps outlined in the confined space entry/rescue permit

## Medical Assessment

- If no EMS is on scene, the firefighter or officer with the highest level of medical training will assume overall responsibility for EMS operations.

- If death is obvious or the patient has been pronounced dead by ALS, the body should not be removed from the confined space. The body should only be removed when the medical examiner or the police officer in charge of the investigation has given the order to remove the body.

## Incident Conclusion

- At the conclusion of the incident, all equipment is to be cleaned and/or decontaminated, checked, and placed back in service in working condition.

- Any damaged equipment shall be placed out of service (OOS) and the appropriate notifications made.

## Incident Debriefing

- A critique shall be held within a reasonable amount of time following the incident to discuss the good and bad aspects of the call and to improve the future operations of the department.

- Due to the high stress that sometimes accompanies incidents, members may feel an increased level of stress following certain responses. Any personnel may request to have a critical incident debriefing performed for their well being. The member may contact an officer to assist in arranging this or can call the appropriate agency themselves. The phone numbers shall be posted in the radio room or can be obtained by calling Somerset County Communications.

CONFINED SPACE RESCUE / ENTRY PERMIT

PHASE 1 – INCIDENT MANAGEMENT SYSTEM (IMS)

| Date: |  |
| --- | --- |
| Incident Address: |  |
| Location of confined space: |  |
| Type of confined space: |  |
| Permit or non-permit required space: |  |

| Incident Commander: |  |
| --- | --- |
| Entry Permit Scribe: |  |
| Operations: |  |
| Safety: |  |
| Haz Mat: |  |
| EMS: |  |
| Accountability Officer: |  |
| Staging Officer: |  |
| Manpower Officer: |  |
| Police Department Officer: |  |
| OEM Representative: |  |

CONFINED SPACE RESCUE / ENTRY PERMIT

PHASE 2 - SIZE UP : Primary Assessment

|  | Meteorological Conditions: Wind Direction: Wind Speed: Is the incident outdoors or indoors: |  |
| --- | --- | --- |
|  | Secure witness: Name: Contact phone number: Description of Incident: |  |
|  | Secure competent person Name: Contact phone number: Description of Incident: |  |
|  | Identify immediate hazards | 1.) 2.) 3.) 4.) 5.) |
|  | Location, number and condition of patient(s) |  |
|  | Time patient(s) last seen alive |  |
|  | Request additional resources Other possible additional resources (request as needed) | BLS (min. 2), ALS (min. 1) Air 28 (breathing air) Ladder 26 (rope/rigging) HazMat 26 (decontamination) Somerset County HazMat (hazardous materials response) Rescue 25 (additional confined space equipment) |
|  | Secure site entry permit from workers (if available) |  |

CONFINED SPACE RESCUE / ENTRY PERMIT

PHASE 2 - SIZE UP : Secondary Assessment

|  | Details on the confined space |  |
| --- | --- | --- |
|  | Diagram of confined space (or secure a diagram from competent person if possible) |  |
|  | Identify Hazardous chemicals or products in confined space | 1.) 2.) 3.) 4.) 5.) |
|  | Identify Hazards - atmospheric |  |
|  | Identify Hazards - electric |  |
|  | Identify Hazards - mechanical |  |
|  | Identify Hazards - pneumatic |  |
|  | Identify Hazards - hydraulic |  |
|  | Identify Hazards - other |  |
|  | Identify Hazards - structural stability |  |
|  | IC decision: Rescue or recovery ? |  |

CONFINED SPACE RESCUE / ENTRY PERMIT

PHASE 3 - PRE-ENTRY OPERATIONS : Secure Scene

|  | Establish hot zone (rescue zone) |  |
| --- | --- | --- |
|  | Establish warm zone (decon) |  |
|  | Establish cold zone (manpower, equipment, etc.) |  |
|  | Establish accountability system and officer |  |
|  | Establish manpower staging areas and officer |  |
|  | Establish apparatus staging areas and officer |  |
|  | Establish tool staging areas (coordinate with operations) |  |
|  | Evacuate bystanders (if necessary) |  |
|  | Traffic/crowd control (assign to PD) |  |

Other Scene Notes and Considerations:

CONFINED SPACE RESCUE / ENTRY PERMIT

PHASE 3 - PRE-ENTRY OPERATIONS : Stage and Check Equipment

|  | Ventilation fans and ductwork | Place in service ASAP |
| --- | --- | --- |
|  | Atmospheric monitoring equipment: 4 gas monitor – monitoring of confined space 4 gas monitor - worn by 1 member of entry team | Place in service ASAP |
|  | Rescuer equipment turnout gear, nomex jumpsuits, BDUs SABA (Scott Escape Pak) knee pads rescue helmets with head lamps eye protection ear protection (if necessary) class 3 full body harness intrinsically safe survivor lights intrinsically safe portable radios with direct channel |  |
|  | SABA Air cart Hoses (use different color for each rescuer) |  |
|  | Continuous breathing air supply air truck or additional bottles for air cart |  |
|  | Retrieval systems tripod hauling system retrieval lines (use different color for each rescuer) rope rescue hardware |  |
|  | Patient removal equipment SKED stokes KED wrist straps |  |
|  | Lockout / tagout LOTO kit on rescue Assign at least 1 rescuer to be responsible for LOTO |  |
|  | Patient Care first responder bag oxygen kit fanny pack for entry team |  |

CONFINED SPACE RESCUE / ENTRY PERMIT

PHASE 3 - PRE-ENTRY OPERATIONS : Secure Rescue Scene

|  | Continue to monitor weather conditions (if applicable) |  |
| --- | --- | --- |
|  | Test atmosphere (outside space) |  |
|  | Oxygen (%) |  |
|  | LEL (%) |  |
|  | Toxic (ppm) |  |
|  | CO (ppm) |  |
|  | Hydrogen Sulfide (ppm) |  |
|  | Test atmosphere (inside space) |  |
|  | Oxygen (%) |  |
|  | LEL (%) |  |
|  | Toxic (ppm) |  |
|  | CO (ppm) |  |
|  | Hydrogen Sulfide (ppm) |  |
|  | Ventilate atmosphere |  |
|  | Secure Hazards (lockout / tagout) |  |
|  | electrical |  |
|  | mechanical |  |
|  | atmospheric |  |
|  | pneumatic |  |
|  | hydraulic |  |
|  | other |  |
|  | Verify (i.e., test, operate) that all hazards are secure |  |
|  | Secure chemical hazards |  |

CONFINED SPACE RESCUE / ENTRY PERMIT

PHASE 4 - RESCUE OPERATIONS

|  | Entry team |  |
| --- | --- | --- |
|  | #1 name / attendant name / retrieval line color |  |
|  | #1 time in / time out |  |
|  | #2 name / attendant name / retrieval line color |  |
|  | #2 time in / time out |  |
|  | Back-up team |  |
|  | #3 name / attendant name / retrieval line color |  |
|  | #3 time in / time out |  |
|  | #4 name / attendant name / retrieval line color |  |
|  | #4 time in / time out |  |
|  | Air Cart Operator name |  |
|  | Contingency plan for rescuers |  |
|  | Pre-entry equipment check |  |
|  | PPE |  |
|  | Intrinsically safe lighting |  |
|  | Intrinsically safe communications |  |
|  | Full body harness (class 3) |  |
|  | Retrieval line and retrieval system |  |
|  | Escape packs connected to air hose (SABA) |  |
|  | Air cart operation |  |
|  | Personal atmospheric monitor with entry team |  |
| Continuous atmospheric monitoring must take place throughout the entire rescue. Use the air monitoring sheet on the last page of this SOG to record the results. |

CONFINED SPACE RESCUE / ENTRY PERMIT

PHASE 4 - RESCUE OPERATIONS

Record the who, what , and when of the rescue. Be as specific as possible.

|  | Patient(s) location |  |
| --- | --- | --- |
|  | Patient(s) assessment |  |
|  | Will the patient require decontamination ? |  |
|  | Patient(s) packaging |  |
|  | Patient(s) extrication |  |
|  | Patient(s) decontamination |  |
|  | Patients treated by what units? Patients transported to where and by whom ? |  |

CONFINED SPACE RESCUE / ENTRY PERMIT

PHASE 5 – INCIDENT TERMINATION

|  | All personnel accounted for |  |
| --- | --- | --- |
|  | Remove tools and equipment |  |
|  | Decontamination of equipment |  |
|  | Secure scene |  |
|  | Station debriefing |  |
|  | Call OSHA |  |

| ID of Firefighter Performing Monitoring: |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Time of Reading: |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Monitor weather conditions (if applicable) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Test atmosphere (outside space) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Oxygen (%) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| LEL (%) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| CO (ppm) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Hydrogen Sulfide (ppm) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| _____________________ (ppm) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Test atmosphere at various levels inside space |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Oxygen (%) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| LEL (%) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| CO (ppm) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Hydrogen Sulfide (ppm) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| _____________________ (ppm) |  |  |  |  |  |  |  |  |  |  |  |  |  |

| ID of Firefighter Performing Monitoring: |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Time of Reading: |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Monitor weather conditions (if applicable) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Test atmosphere (outside space) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Oxygen (%) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| LEL (%) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| CO (ppm) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Hydrogen Sulfide (ppm) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| _____________________ (ppm) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Test atmosphere at various levels inside space |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Oxygen (%) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| LEL (%) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| CO (ppm) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Hydrogen Sulfide (ppm) |  |  |  |  |  |  |  |  |  |  |  |  |  |
| _____________________ (ppm) |  |  |  |  |  |  |  |  |  |  |  |  |  |